## Slide 1
SCIENCE MEETS CIRCUITS
Router basics,routing protocols,and security basics
Routing & Security
Notes: 1

## Slide 2
PRESENTER
DEPARTMENT
ECE Level 300
POSITION
Network Camp Instructor
CONTACT
ranahythmhsny@gmail.com
Rana Haitham
Notes: 1

## Slide 3
BOOT SEQUENCE
AGENDA
01
Router Basics
What is router ? ,router hardware ,router modes & basic configuration.
02
Routing
Routing types,static route & default route.
03
Dynamic route
admin. distance ,Types dynamic route,RIP,EIGRP,OSPF.
04
Access control list (ACL)
ACL types ,ACL configuration
AGENDA
Notes: 2

## Slide 4
BOOT SEQUENCE
AGENDA
06
Etherchannel & DHCP snooping
05
Spanning Tree Protocol (STP)
STP, port fast , & port security.
Notes: 2

## Slide 5
What is router?
A router is a network device that forwards data packets between different computer networks,
directing Internet traffic to ensure data reaches its correct destination
01
02
Router components
Router Basics
  Serial ports: Connect WAN links and routers.
  Console port: Used for initial router configuration.
  Auxiliary port: Allows remote dial-in management.
  FastEthernet ports: Connect high-speed LAN devices.
  Power switch & Power card connection: Supplies and controls power.
Notes: 2

## Slide 6
BOOT SEQUENCE
Router Basics
Router Hardware
03
  ROM: Read-only memory that contains the bootstrap program, power-on self-test
(POST) diagnostics, and a mini-IOS for recovery.
  Flash Memory: Non-volatile memory used to store the router's operating system
(Cisco IOS) image file and system files.
  RAM: Volatile memory that stores the running configuration file (running-config),
routing tables, and ARP cache while powered on.
  NVRAM: Non-volatile memory that stores the permanent startup configuration file
(startup-config) and configuration register.
Notes: 2

## Slide 7
MODULE 01
Router Basic configuration
Router modes
User EXEC Mode
  Description: Basic view-only mode for simple diagnostics.
  Prompt: Router>
Privileged EXEC Mode (Enable Mode)
  Description: Provides full diagnostic (show/debug) and management access.
  Prompt: Router#
Global Configuration Mode
  Description: Used to modify global system-wide settings.
  Prompt: Router(config)#
Specific Configuration Modes (Submodes)
  Description: Submodes used to configure specific interfaces, lines, or protocols.
  Prompts: Router(config-if)#, Router(config-line)#, Router(config-router)#
MODULE 01
Notes: 3

## Slide 8
MODULE 02
Static Route
Manual (configured by the administrator).
Saves CPU, RAM, and bandwidth.
Dynamic Route
Configured automatically via protocols.
Routing
Consumes processing power and bandwidth.
Small or simple networks.
Medium to large, complex networks.
Manual rerouting required on link failure.
Automatic failover and instant rerouting.
Notes: 4

## Slide 9
Routing
Administrative Distance (AD)
Definition: A numerical value (0 to 255) used by routers to measure
the trustworthiness of a routing source.
Rule: The lower the AD value, the more trusted the route.
Common AD Values:
Directly Connected: 0 EIGRP: 90
Static Route: 1 OSPF: 110
RIP: 120
Autonomous System (AS)
  Definition: A collection of networks under a single administrative domain (e.g., a company, university, or ISP).
  Protocol Classification:
    IGP (Interior Gateway Protocols): Used within an AS (OSPF, EIGRP, RIP).
    EGP (Exterior Gateway Protocols): Used between different AS across the Internet (BGP).

## Slide 10
FIELD LOG
GALLERY
Dynamic Route
Exterior
  Used between different Autonomous Systems (AS).
  Example: BGP (Border Gateway Protocol)
Interior
  Used within a single Autonomous System (AS).
Distance Vector
Link-State
Hybrid
  Metric: Hop Count
  Examples: RIP, RIPv2
  Metric: Composite Metric (Bandwidth + Delay)
  Examples: EIGRP
  Metric: Bandwidth & Speed
  Examples: OSPF
Notes: 5

## Slide 11
FIELD LOG
GALLERY
RIP &RIPv2
EIGRP
OSPF
Routing protocols
  Administrative Distance (AD): 120
  Subnetting (VLSM) Support:
RIPv1: No (Classful)
RIPv2: Yes (Classless)
  Multicast IP:
RIPv1: Broadcast (255.255.255.255)
RIPv2: 224.0.0.9
  Update Interval: Periodic every 30 seconds
  Administrative Distance (AD): 90
  Subnetting (VLSM) Support: Yes (Classless)
  Multicast IP: 224.0.0.10
  Update Interval: Triggered / Partial updates (Only when topology changes)
  Administrative Distance (AD): 110
  Subnetting (VLSM) Support: Yes (Classless)
  Multicast IP: 224.0.0.5 (All Routers) / 224.0.0.6 (DR/BDR)
  Update Interval: Triggered / Partial updates (Refreshed every 30 minutes)
Notes: 5

## Slide 12
FIELD LOG
GALLERY
OSPF Process & LSA
DR & BDR Election
Router ID Selection
OSPF Operation & Core Concepts
  LSA
Routers exchange link-state
advertisements to share link status
and network topology.
  LSDB
All LSAs combine into a shared
topology map.
  SPF
Dijkstra’s algorithm runs on the
LSDB to find the shortest path.
  Purpose: Reduce routing-update traffic on multi-access broadcast networks.
  1 · Interface priority
Highest wins; default 1. Priority 0 is
ineligible for DR or BDR.
  2 · Router ID
Highest wins when priorities tie.
  Manual: Configured with the router-id command.
  Loopback: Highest IP on an active loopback interface.
  Physical: Highest IP on an active physical interface.
Notes: 5

## Slide 13
FIELD LOG
ACCESS-Control List
Standard ACL
  Number Range: 1 – 99
  Filtering Basis: Filters traffic based ONLY on Source IP Address.
  Control Action: Permits or Denies the entire packet/traffic (cannot filter specific protocols or port numbers).
  Placement Strategy: Placed as CLOSE TO DESTINATION as possible.
  Types & Naming: Available as both Numbered ACL and NamedACL.
Extended ACL
  Number Range: 100 – 199
  Filtering Basis: Filters based on Source IP, Destination IP, Protocol (TCP/UDP), and Port Numbers.
  Control Action: Granular control (can block specific services like HTTP/Port 80, SSL/Port 22, etc.).
  Placement Strategy: Placed as CLOSE TO SOURCE as possible.
  Types & Naming: Available as both Numbered ACL and NamedACL.
GALLERY
Notes: 5

## Slide 14
FIELD LOG
Spanning Tree Protocol & Port Security Essentials
Spanning Tree Protocol (STP)
  Purpose: Prevents Layer 2 switching loops in redundant network topologies by blocking redundant paths dynamically.
  Root Switch Election:
    Switch with the Lowest Bridge ID (BID) becomes Root.
    Bridge ID = Priority + MAC Address.
  Root Port (RP) Selection:
    Chosen on non-root switches based on the Lowest Path Cost to the Root Switch.
STP PortFast
  Purpose: Accelerates edge port convergence for end-user devices (PCs, Printers, Servers).
  Functionality:
    Bypasses Listening and Learning states.
    Immediately places access ports into the Forwarding state upon connection.
  Key Advantage: Reduces network downtime and DHCP lookup delays.
Port Security
  Purpose: Protects Layer 2 switch ports against unauthorized device connections.
  Functionality: Restricts access based on MAC addresses (Static, Dynamic, or Sticky).
  Violation Actions:
    Shutdown: Disables port completely upon violation.
    Restrict / Protect: Drops unauthorized traffic and logs alerts.

## Slide 15
FIELD LOG
EtherChannel & DHCP Security
EtherChannel
  Definition: Link-aggregation technology that combines multiple physical Ethernet links into a single logical high-speed link.
  Core Purpose:
    Increases total bandwidth and provides link redundancy.
    Load-balances traffic across physical links.
  Key Advantage: Prevents STP topology recalculations when an individual physical link in the bundle fails.
DHCP Security (Attack & Solution)
  The Threat — DHCP Spoofing:
    A rogue (unauthorized) DHCP server responds to client requests with malicious IP settings, redirecting traffic (Man-in-the-Middle attack).
  The Solution — DHCP Snooping:
    Layer 2 security mechanism that filters untrusted DHCP messages.
    Designates switch ports as Trusted (legitimate DHCP server) or Untrusted (end-user ports).
    Builds a Binding Database to validate network hosts and block malicious responses.

## Slide 16
Recap & Summary
Router Basics & Routing Protocols
Router Operations & Initial Setup Configuration.
Routing Protocols Covered:
RIPv2, EIGRP, and OSPF.
Traffic Control & Security (ACLs)
  Access Control Lists: Standard vs. Extended ACLs.
  Configuration using Numbered and Named ACLs.
Switch Security
Loop Prevention: STP & STP PortFast.
Switch Hardening: Port Security & DHCP Snooping against DHCP Spoofing.
Performance: EtherChannel for Link Aggregation.
FIELD LOG

## Slide 17
Quick Knowledge Check
Q1 · ROUTING PROTOCOLS
Which routing protocol uses Area concepts and calculates paths using Dijkstra's algorithm?
  A) RIPv2
  B) EIGRP
  C) OSPF
Answer: C
Q2 · ACCESS CONTROL LISTS
Where should a Standard ACL be placed for optimal traffic filtering?
  A) As close to the Source as possible.
  B) As close to the Destination as possible.
Answer: B
Q3 · LAYER 2 & STP
What is the main advantage of enabling STP PortFast on access ports?
  A) Increases bandwidth.
  B) Immediately transitions ports to Forwarding state, bypassing Listening/Learning.
Answer: B
Q4 · SWITCH SECURITY
Which security feature mitigates Rogue DHCP servers and DHCP Spoofing attacks?
  A) Port Security
  B) DHCP Snooping
  C) EtherChannel
Answer: B
FIELD NOTE

## Slide 18
ANY QUESTIONS?
system.query( ) awaiting input...
( don't be like Chrome — ask before you fall behind )
Q & A
Notes: 7

## Slide 19
THANK YOU
Notes: 8